## Slide 1
Tracker Overview
August 05, 2020
Ananthesh J Shet
Technical Leader

## Slide 2: Presenter
Ananthesh J Shet
9+ year in Delphi/APTIV
Autocoding
Embedded Software – ESR2.5, SRR2, SRR3
Tracker Algorithm – GDSR, U360(Radar-Camera)
Currently leading Sensor Modelling team – SRR5

## Slide 3: General Overview
TRACKER
Vehicle Data
Detections
Objects
Filter which can also predict
Sensor

## Slide 4: GDSR Tracker
Tracklet Tracker
Grouping
Object Tracker
Vehicle Data
Vehicle Processing
Detections
Detection Processing
Coordinate Conversion, Motion Status, Identify undesired detections
Speed, Curvature
Various trackers came into being to cater for different needs
Tracklet
Object

## Slide 5: Tracklet Tracker
Time Update (Predict)
Data Association (Association)
Status Update (Update)
Previous tracklets are time updated
Detections are associated(matched) to time updated tracklets. New tracklets are formed from unmatched detections
Tracklets are updated based on matched detections
Detection
Tracklet
One to one
Fixed Gain KF, Constant Turn model

## Slide 6: Kalman Filter
An object is at x position = 10m
x_pos
12m
x_pos
13m
x_pos
12.8m
0
Values only for demonstartion
Prediction
Measurement
Update
Probability
Probability
Probability

## Slide 7: Grouping
Sensor 1 tracklet
Sensor 2 tracklet
Associate tracklets to group
Create new groups
Group groups

## Slide 8: Object Tracker
Time Update (Predict)
Data Association (Association)
Status Update (Update)
Previous objects are time updated
Tracklets are associated(matched) to time updated objects. New objects are formed from unmatched tracklets
Objects are updated based on matched tracklets
Data association here is part of Grouping
Fixed Gain KF, Constant Acceleration model

## Slide 9: Object Tracker
Time Update (Predict)
Data association
Status Update (Update)
Previous objects are time updated
Tracklets are associated(matched) to time updated objects. New objects are formed from unmatched tracklets
Objects are updated based on matched tracklets
If grouping creates a NEW object, the Object Tracker “Update” will update the object to MATURE
Tracklet Tracker

## Slide 10: Example(using MATE – Matlab based Automated Testing Environment)
Log: C:\Project\Logs\SRR5\BMW\20191023_LOW_A310_SENSORS\SRR_Specific_Data_RAW_DEBUG_LOW\LOW_3.8.201_check_20min_WBACR61010LH94641_20191023_095829_WR3_0036_ORCAS.mf4
Position: FRONT_LEFT_ORIG
Start timeindex: 42, detection id: 36, tracklet id: 4
Timeindex: 44, Object id 31 is formed
Timeindex: 47, tracklet id 2 gets associated to object id 31

## Slide 11: Wrappers around the tracker
Heading
Guardrail detector
Cloud processing - Clustering
Countermeasures
      Terminate long coasted entity
      Terminate Stationary entity
      Terminate entities behind guardrail
      Terminate ghosts – low probability, eclipsed
Add derived signals
      Reference points
      Object Amplitude
      Object class – Size, speed, wheelspin
2nd order Guardrail
Cloud
Reference points
Truck
Car
Two Wheeler
Pedestrian
Class

## Slide 12: What can go wrong?
Mounting position
Alignment
Calibration
Async vehicle data
Reality
Calibration
VehicleData | Detection
Timestamp N | Timestamp N-2
Timestamp N+1 | Timestamp N-1
Timestamp N+2 | Timestamp N
Timestamp N+3 | Timestamp N+1
VehSpeed = 20m/s
YawRate = 1deg/s
DetRangeRate = 10m/s
Azimuth = 30deg
Timestamp N
VehSpeed = 18m/s
YawRate = 2deg/s
DetRangeRate = 8m/s
Azimuth = 32deg
Timestamp N+1
Mounting/Alignment errors
Async vehicle data

## Slide 13
THANK YOU!