## Slide 1
RESIM Supported modes
March 12, 2024
Pavan Jaggarapu
Senior Software Engineer

## Slide 2: SRR Radar Core Architecture
Core1(Z7A)
Core2(Z7B)
Core0(Z4)
Ethernet
CAN FD
Feature Function State Machines
Tracking Algorithm
FEATURE Algorithms
IPC
IPC
Signal Processing Algorithms
Angle Finding Algorithm
Flexray/CAN Comm
IPC
OS Sync
Logging
AUTOSAR
CAN FD
Vehicle
Private

## Slide 3: SIL Data Injection and Entry Points
CDC Mode – CDC Injection
  CDC data injected into Core 1
  Used for debugging Core 1 Signal processing.
  Verify Core 1 Detections & Core 2 - Tracks and Feature Functions.
Detection Mode - Injection of Detections
  Detections injected into Core 2 .
  Used to Debug Tracker, Fusion and Feature functions
  Debugging can be started from Tracks .
DSpace Mode - Injection of Simulated Detections
  Simulated Detections from DSpace are Injected into Core 2 Tracker Inputs .
  Used to debug Tracker, Fusion and Feature Functions.
  Debugging can be started from Tracks .

## Slide 4
SIL (CDC Injection Mode for Verification from Signal Processing Onwards )
ADC
RDD 1st Pass
RDD 2nd Pass
Angle Finding
IPC
OS
CAN FD
Detections ,Tracks, Feature Output
Feature Functions
Detections
IPC
Tracker
UDP Logs
MF4/ DVSU
BINARY
(Dets, Tracks , FF)

## Slide 5
ADC
RDD 1st Pass
RDD 2nd Pass
Angle Finding
IPC
OS
CAN FD
Detections, Tracks, Feature Output
Feature Functions
Detections
IPC
Tracker
UDP Logs
MF4 /DVSU
BINARY
(Dets, Tracks , FF)
SIL ( Detections Injection Mode for Tracker / FF Verification )

## Slide 6
ADC
RDD 1st Pass
RDD 2nd Pass
Angle Finding
IPC
OS
CAN FD
Detections, Tracks, Feature Output
Feature Functions
Detections
IPC
Tracker
Dspace Simulated Detections
MF4 /DVSU
BINARY
(Dets, Tracks , FF)
SIL ( DSpace Injection Mode for Tracker / FF Verification )